## Slide 1: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen

## Slide 2: Traditional Method
IC
PC
Computer sends all settings to the DUT (in arbitrary order) for measurement.
A constellation of all settings is generated.
Computer scans all constellation points to find the point closest to the ideal position and establish the mapping.
Advantage:
Highest accuracy and often guaranteed solution.
Measurement order and details of the controls are hidden from the user.
Relaxed requirement for the DUT gain and phase response.
Disadvantage:
Long measurement time and long post-processing time. (Need to measure every point and computer need to scan every point for comparison for every ideal points)

## Slide 3: Adaptive Measurements

## Slide 4: Adaptive Measurements

## Slide 5: Adaptive Measurements
Need bi-directional relationship from DUT settings to the measurement points.
DUT response need to be predictable, and the measurement results need to be near the ideal points.

## Slide 6: Outphasing Phase Shifter

## Slide 7: Outphasing Phase Shifter

## Slide 8: Outphasing Phase Shifter

## Slide 9: Outphasing Phase Shifter

## Slide 10: Outphasing Phase Shifter

## Slide 11: Outphasing Phase Shifter

## Slide 12: Outphasing Phase Shifter

## Slide 13: Outphasing Phase Shifter

## Slide 14: Outphasing Phase Shifter

## Slide 15: Outphasing Phase Shifter
Vector Phases to Cartesian:
Cartesian to Vector Phases:
(using inverse kinematic)

## Slide 16: Outphasing Phase Shifter
Vector Phases to Cartesian:
Cartesian to Vector Phases:
(using inverse kinematic)

## Slide 17: RFVM
Vector lengths to Cartesian:
Cartesian to Vector lengths:

## Slide 18: Adaptive Measurements
ideal target point
For an ideal target point, use inverse kinematic to calculate the corresponding two vector phases and obtain the measurements.

## Slide 19: Adaptive Measurements
ideal target point
For an ideal target point, use inverse kinematic to calculate the corresponding two vector phases and obtain the measurements.
measurements
If measure all the points for a constant gain circle at once, the distorted circle makes adjustment difficult and reductant measurements are made.

## Slide 20: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0

## Slide 21: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 22: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 23: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 24: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 25: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 26: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 27: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.

## Slide 28: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.

## Slide 29: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution)

## Slide 30: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution)

## Slide 31: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.

## Slide 32: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.

## Slide 33: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
  is targeting point inside the measurement results boundary?

## Slide 34: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 35: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 36: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 37: Point-to-Point Progressive Measurements

## Slide 38: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 39: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 40: RTPS Phase Switching Modes
RTPS 1
RTPS 2
RTPS 3
RTPS 1
RTPS 2
RTPS 3

## Slide 41: RTPS Phase Switching Modes

## Slide 42: RTPS Phase Switching Modes

## Slide 43: RTPS Phase Switching Modes

## Slide 44: RTPS Phase Switching Modes
RTPS 1
RTPS 2
RTPS 3
RTPS 1
RTPS 2
RTPS 3
9 Modes for a pair of phase setting.
Due to PVT variation and mismatch, the constellation of the 9 modes are slightly different.
Provide fine tune to the constellation point.
Due to the random nature of this variation, this effect cannot be learned.

## Slide 45: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 46: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 47: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 48: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.

## Slide 49: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.

## Slide 50: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.
  Establish mapping between the codeword of the closest point to the position of the ideal point.

## Slide 51: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.
  Establish mapping between the codeword of the closest point to the position of the ideal point.
  Repeat 2 until all ideal points on this gain circle are calibrated.

## Slide 52: Point-to-Point Progressive Measurements
Remarks:
Progressive measurement is repeated for every needed constant gain circle.
The step of phase offset compensation should be done after DC offset compensation and vector length measurement.
All measurement results in the search area are saved so that there is no need for repetitive measurement when accessed again.

## Slide 53: Accelerated Measurement Prediction

## Slide 54: Accelerated Measurement Prediction

## Slide 55: Accelerated Measurement Prediction

## Slide 56: Accelerated Measurement Prediction

## Slide 57: Accelerated Measurement Prediction
Mapping

## Slide 58: Accelerated Measurement Prediction

## Slide 59: Accelerated Measurement Prediction

## Slide 60: Accelerated Measurement Prediction

## Slide 61: Accelerated Measurement Prediction

## Slide 62: Accelerated Measurement Prediction

## Slide 63: Accelerated Measurement Prediction

## Slide 64: Accelerated Measurement Prediction

## Slide 65: Accelerated Measurement Prediction

## Slide 66: Accelerated Measurement Prediction
Target Position
Ideal Position that results in the closest measurement to the target position

## Slide 67: Accelerated Measurement Prediction
Target Position
Ideal Position that results in the closest measurement to the target position
In-situ training and validating

## Slide 68: Accelerated Measurement Prediction

## Slide 69: Accelerated Measurement Prediction

## Slide 70: Accelerated Measurement Prediction

## Slide 71: Accelerated Measurement Prediction

## Slide 72: Accelerated Measurement Prediction
Target Position
Ideal Position that results in the closest measurement to the target position
In-situ training and validating
Progressive training per gain circle.
Neural Network replaces the normal routine after making 5 correct prediction in a row.
When the network is not validated, a new targeting point is fed to the neural network for testing before it is used for training so that the testing data has not been trained by the network.
Neural Network prediction is verified by doing the 9 mode measurements and judge if the closet point is close enough (by previous standard).
If Neural Network prediction is checked to be inaccurate, the current targeting point is calibrated using the normal routine and the neural network restart training.

## Slide 74: Thank you

## Slide 75: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Development Update 1

## Slide 76: Demo

## Slide 77
Calibration Result (Single Mode)

## Slide 78
Traditional Method (Single Mode)

## Slide 79
Measurement non-uniformity causes distortion in constant gain circle

## Slide 80
Measurement non-uniformity causes distortion in constant gain circle
Causes the measurement points to go to unexpected locations.
Causes measurement dead zones.
Distortion gets weaker as the gain circle radius increases.
Expect to see RMS errors gets better for larger gain circles. (Verified)

## Slide 81
Measurement Dead zones

## Slide 82
Measurement Dead zones
Decrease the gain and phase steps in the search kernel (to below the theoretical resolutions).
Use absolute value instead of dB for gain resolution.
Implement adaptive gain resolution (observe no improvement).
For each ideal point, search for the two inverse kinematic solutions which doubles the number of measurements.

## Slide 83
Measurement Dead zones

## Slide 84
Measurement Dead zones

## Slide 85
Crossing the sea
Adaptively increase the search area kernel size if the program is stuck on calibrating an ideal point for too long.
Filter the measurement results and remove outliers for kernel validation.

## Slide 86: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Development Update 2

## Slide 87
Calibration for individual gain and phase control chain
8-bit VGA and 8-bit phase shifter
256*256 = 65536 points
Phase corrected to reference the phase of “0” phase setting for each gain settings.

## Slide 88
Gain Profile Characterization
For better initial guess of the gain index for a targeting gain.
Gain profile is scaled by the max gain ratio in the targeting phase direction.

## Slide 89
Chart: 
| Kernel Search | Traditional
Column3 | 5593 | 65536
Number of Measurement

## Slide 90
Chart: 
|  |  | Kernel Search | Traditional
Column3 | 783 | 1170 | 5593 | 65536
Number of Measurement

## Slide 91: Demo

## Slide 92
Chart: 
| Machine Learning | Optimization | Kernel Search | Traditional
Column3 | 783 | 1170 | 5593 | 65536
Number of Measurement

## Slide 93
For calibrating 7 gain circles of 64 points each
Traditional:
  65536 points measured
  146.3 measurement per point
Kernel Search:
  5593 points measured (275 for pre-characterization)
  12.5 measurement per point (11.9 excluding the pre-characterization)
Single-Point Optimization + Kernel Search:
  1170 points measured (275 for pre-characterization)
  2.6 measurement per point (2 excluding the pre-characterization)
Machine Learning + Single-Point Optimization + Kernel Search:
  783 points measured (275 for pre-characterization)
  1.75 measurement per point (1.13 excluding the pre-characterization)

## Slide 94
Single-Point Optimization
For well-behaved variable-gain phase shifter and relaxed RMSE requirement, single-point optimization method often arrive to an acceptable point in less step than the measurement needed for a kernel search.
If optimization cannot find an acceptable point within certain steps, then the kernel search activates.

## Slide 95
Machine Learning for accurate first guess
A baseline model is trained with a vast amount of measurement data of a single PS type.
  Normalized gain and phase-corrected and normalized phase.
  Gain from 0 to 1. Phase from 0 to 1.
The baseline model continue to incrementally train using the new measurement data for adaption.

## Slide 96: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Development Update 3

## Slide 97
Vector Sum
Two 6-bit VGA
64*64 = 4096 points
Constellation not rotated in consideration of constellation rotation mismatch in array level calibration.

## Slide 98
For calibrating 7 gain circles of 64 points each
Traditional:
  65536 points measured
  146.3 measurement per point
Kernel Search:
  5593 points measured (275 for pre-characterization)
  12.5 measurement per point (11.9 excluding the pre-characterization)
Single-Point Optimization + Kernel Search:
  1170 points measured (275 for pre-characterization)
  2.6 measurement per point (2 excluding the pre-characterization)
Machine Learning + Single-Point Optimization + Kernel Search:
  783 points measured (275 for pre-characterization)
  1.75 measurement per point (1.13 excluding the pre-characterization)

## Slide 99
For calibrating 7 gain circles of 64 points each
1.75 1.13
Total Excluding Pre-characterization

## Slide 100
For calibrating 7 gain circles of 64 points each
1.24 0.99
Total Excluding Pre-characterization

## Slide 101: Demo

## Slide 102
Total Phase RMSE: 1.102 degrees
Total Gain RMSE: -23.779 dB
This Algorithm: 556 measurements
Total Phase RMSE: 0.884 degrees
Total Gain RMSE: -24.201 dB
Traditional: 4096 measurements

## Slide 103
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 104
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 105
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 106
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 107
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 108
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 109
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 110
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 111
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 112
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 113
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 114
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 115
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 116
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 117
Vector Sum Pre-characterization
Need a reference point as the origin of the two vectors
Need the direction of the two vectors
Need a profile to predict the index/code needed to get to a specific vector length

## Slide 118
Vector Sum Pre-characterization
Reference point doesn’t need to be at DC offset > No need for measuring DC offset
The vector profile near the reference point need to be well defined > select reference point near the center of the constellation but it doesn’t have to be THE CENTER.

## Slide 121: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Phase One Summary

## Slide 122
Sneak Peek

## Slide 123
Outphasing: Pre-Characterization
DC Offset:
Set two vectors to have the same setting and sweep a circle.
Calculate the average of all the measured points
cartesian point from summing vectors of angle i and j (ideal position)
cartesian point from measuring (measurement position)

## Slide 124
Outphasing: Pre-Characterization
DC Offset Compensation:
Subtract the targeting point by the DC offset point.

## Slide 125
Outphasing: Pre-Characterization
Vector Length:
For a constant angle of one vector, sweep the other vector.
Find the center of each circle by finding the average of the measurements on each circle.
cartesian point of circle center whose angle to the DC offset is i.

## Slide 126
Outphasing: Pre-Characterization
Vector Length:
For a constant angle of one vector, sweep the other vector.
Find the center of each circle by finding the average of the measurements on each circle.
Find average radius of each circle.
average radius of circle with center of

## Slide 127
Outphasing: Pre-Characterization
Phase Offset:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 128
Outphasing: Pre-Characterization
Phase Offset:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 129
Separate-Indexing
Gain index
Phase index

## Slide 130
Separate-Indexing: Pre-Characterization
Sampling Gain index: {end}
Sampling Phase index: {round(linspace(1,end,steps))}
……

## Slide 131
Separate-Indexing: Pre-Characterization
Sampling Gain index: {end}
Sampling Phase index: {round(linspace(1,end,end))}
……
Note that the phase index “j” is treated as a constant

## Slide 132
Separate-Indexing: Machine Learning
Use machine learning as another way of translating targeting position to index.
Machine learning model, if properly trained, can accurately model non-idealities that would otherwise be difficult to model by pre-characterization.
The machine learning model should be trained on a general dataset of a type of variable-gain phase-shifters that all exhibit similar behaviors so the model could quickly adapt to a specific device.
Use normalized values for training so that the model can be easily applied to different devices.
Normalized Phase-Corrected Measurement Polar Coordinates

## Slide 133
Separate-Indexing: Machine Learning
Phase Offset Compensation:
Subtract the targeting phase by the phase offset.

## Slide 134
Separate-Indexing: Machine Learning
Trained on 65536 data points
  Randomly shuffled
  0.7 train, 0.15 val, 0.15 test
Trained on CPU using MATLAB fitnet and default options
  The optimization function supported on GPU produce worse result
Hidden layer size of 15 is chosen for best observed performance
~ 88% first point accuracy

## Slide 135
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 136
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
Vector-Sum: Pre-Characterization

## Slide 137
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
Vector-Sum: Pre-Characterization

## Slide 138
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 139
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 140
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]

## Slide 141
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The direction of the two vectors should be defined at where the constellation points are the densest.

## Slide 142
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The direction of the two vectors should be defined at where the constellation points are the densest.
Usually this is at the center of the constellation.

## Slide 143
Vector-Sum: Pre-Characterization
  Sample the vector in multiple parts for generalization.

## Slide 144
Vector-Sum: Pre-Characterization
  Sample the vector in multiple parts for generalization.

## Slide 145
Vector-Sum: Pre-Characterization
)

## Slide 146
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 147
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 148
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 149
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Individually scale each side of the constellation for maximum accuracy.

## Slide 150
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Individually scale each side of the constellation for maximum accuracy.

## Slide 151: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Phase One Summary

## Slide 152
Formulation

## Slide 155
Outphasing

## Slide 156
Outphasing

## Slide 157
Outphasing

## Slide 158
Separate Indexing

## Slide 159
Separate Indexing

## Slide 160
Separate Indexing

## Slide 161
Vector Sum

## Slide 162
Vector Sum

## Slide 163
Vector Sum

## Slide 164
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Measurement
Measurement Point Position
Point Finding
Next*

## Slide 165
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Unique for different types of variable gain phase shifters
Provides a first guess of the code/index
Established through:
  Pre-characterization
    DC offset, vector length, phase offset, index-to-position profile
  Machine Learning

## Slide 166
Calibration Mechanism
Next ideal Point Position
Point Finding
Measurement
Same for different types of variable gain phase shifters (it’s based on cartesian coordinates)
Only needed if the first guess doesn’t satisfy specified requirements
Include:
  Measurement filtering and validation
  Adaptive kernel search
  Kernel space mapping

## Slide 167
Two Types of Solution
  Solution by Encirclement
The closest measurement point is chosen if the ideal point is enclosed by the measurements from the kernel.
Only needed if all measurement points from the kernel fails the vicinity test.
Guarantee best solution if the constellation mapping is continuous.
Solution by Vicinity
A measurement point is chosen if it is close enough to the ideal position by a specified standard.
Faster and less measurement needed.

## Slide 168
Shapes of Constellation
Fully-Filled Circular
Fully-Filled
Distorted Circular
Fully-Filled
Distorted Square

## Slide 169
Partially-Filled Circular
Partially-Filled
Distorted Circular
Fully-Filled
Distorted Square
Lower gain is bounded by lowest gain setting in Separate indexing
Shapes of Constellation

## Slide 170
Array Level Phase Offset Mismatch

## Slide 171
Array Level Phase Offset Mismatch

## Slide 172
Array Level Phase Offset Mismatch

## Slide 173
Array Level Phase Offset Mismatch
Set zero-index phase of branch 1 as phase reference.
Global constellation rotation of phase reference.

## Slide 174
Array Level Phase Offset Mismatch
Set zero-index phase of branch 1 as phase reference.
Global constellation rotation of phase reference.

## Slide 175
Array Level Phase Offset Mismatch

## Slide 176
Array Level Phase Offset Mismatch
Notes: 30 10 -20 15 -15

## Slide 177
Array Level Phase Offset Mismatch
Set zero-index phase of branch 1 as phase reference.
Global constellation rotation of phase reference.
Notes: 30 10 -20 15 -15

## Slide 178
Array Level Phase Offset Mismatch
Set zero-index phase of branch 1 as phase reference.
Global constellation rotation of phase reference.
Notes: 30 10 -20 15 -15
-40 -10 -45 -15
0 30 -5 25

## Slide 179
Point Translation

## Slide 180
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 181
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 182
Outphasing
Cartesian to Vector Phases:

## Slide 183
Outphasing
Cartesian to Vector Phases:

## Slide 184
Outphasing
Cartesian to Vector Phases:

## Slide 185
Outphasing
For accurate first guess:
Need to reference points to DC offset
Need accurate vector lengths L1 and L2
Need to compensate for the two vector’s phase offset

## Slide 186
Outphasing
For accurate first guess:
Need to reference points to DC offset
Need accurate vector lengths L1 and L2
Need to compensate for the two vector’s phase offset

## Slide 187
Outphasing: Pre-Characterization
DC Offset:
Causes global positional translation.

## Slide 188
Outphasing: Pre-Characterization
DC Offset:
Causes global positional translation.

## Slide 189
Outphasing: Pre-Characterization
DC Offset Measurement:
Set two vectors to have the same setting and sweep a circle.
[0 0; pi/2 pi/2; pi pi; 3*pi/2 3*pi/2; pi/4 pi/4; 3*pi/4 3*pi/4; 5*pi/4 5*pi/4; 7*pi/4 7*pi/4]

## Slide 190
Outphasing: Pre-Characterization
DC Offset Measurement:
Set two vectors to have the same setting and sweep a circle.
Calculate the average of all the measured points
cartesian point from summing vectors of angle i and j (ideal position)
cartesian point from measuring (measurement position)

## Slide 191
Outphasing: Pre-Characterization
DC Offset Compensation:
Subtract the targeting point by the DC offset point.

## Slide 192
Outphasing: Pre-Characterization
Vector Length Measurement:
For a constant angle of one vector, sweep the other vector.

## Slide 193
Outphasing: Pre-Characterization
Vector Length Measurement:
For a constant angle of one vector, sweep the other vector.
Find the center of each circle by finding the average of the measurements on each circle.
cartesian point of circle center whose angle to the DC offset is i.

## Slide 194
Outphasing: Pre-Characterization
Vector Length Measurement:
For a constant angle of one vector, sweep the other vector.
Find the center of each circle by finding the average of the measurements on each circle.
Find average radius of each circle.
average radius of circle with center of

## Slide 195
Outphasing: Pre-Characterization
Vector Length Measurement:
For a constant angle of one vector, sweep the other vector.
Find the center of each circle by finding the average of the measurements on each circle.
Find average radius of each circle.
Calculate L1/L2 by averaging radius of average radii.

## Slide 196
Outphasing: Pre-Characterization
Vector Length Measurement:
For a constant angle of one vector, sweep the other vector.
Find the center of each circle by finding the average of the measurements on each circle.
Find average radius of each circle.
Calculate magnitude scaling factor (M) for normalizing reading.
Calculate L1/L2 by averaging radius of average radii.

## Slide 197
Outphasing: Pre-Characterization
Phase Offset:
Phase reference is set to the phase of the measurement injection signal.
Phase delay from the injection signal to the measurement instrument causes global phase offset.
In the case of outphasing phase-shifters, the phase mismatch between the two branches also count toward phase offsets and are to be individually compensated.
The vector lengths are known, and the target points are DC offset compensated.
The global phase offset will cause rotation of the constellation and the phase mismatch between the two branches will cause gain error.

## Slide 198
Outphasing: Pre-Characterization
Phase Offset:
Phase reference is set to the phase of the measurement injection signal.
Phase delay from the injection signal to the measurement instrument causes global phase offset.
In the case of outphasing phase-shifters, the phase mismatch between the two branches also count toward phase offsets and are to be individually compensated.
The vector lengths are known, and the target points are DC offset compensated.
The global phase offset will cause rotation of the constellation and the phase mismatch between the two branches will cause gain error.

## Slide 199
Outphasing: Pre-Characterization
Phase Offset:
Phase reference is set to the phase of the measurement injection signal.
Phase delay from the injection signal to the measurement instrument causes global phase offset.
In the case of outphasing phase-shifters, the phase mismatch between the two branches also count toward phase offsets and are to be individually compensated.
The vector lengths are known, and the target points are DC offset compensated.
The global phase offset will cause rotation of the constellation and the phase mismatch between the two branches will cause gain error.

## Slide 200
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.

## Slide 201
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.

## Slide 202
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.

## Slide 203
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 204
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 205
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 206
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 207
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 208
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 209
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 210
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 211
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 212
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 213
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 214
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 215
Outphasing: Pre-Characterization
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phases needed to get to the measured point.
Iteratively compensate for this phase offset until the measured point pass the vicinity test of the ideal point.

## Slide 216
Outphasing: Pre-Characterization
Phase Offset Compensation:
Subtract the targeting phases by their corresponding phase offset.

## Slide 217
Outphasing: Index Mapping
Linear Mapping
is device specific.
Follow 1-to-1 linear mapping between the compensated phases for a phase shifter to its index range.
For two phase shifters each covers 360 degree:

## Slide 218
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 219
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 220
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 221
Separate-Indexing
Gain index
Phase index

## Slide 222
Separate-Indexing
Gain index
Phase index

## Slide 223
Separate-Indexing
Pre-Characterization:
Need to measure the phase offset.
Need to measure the gain and phase profiles so we can predict accurately the index needed to go to a certain gain and phase.
Ignore DC offset as DC offset for this type of variable-gain phase shifter is small.
  The effect of DC offset will by captured by the profiles as long as the DC offset doesn’t exceed the smallest gain circle.

## Slide 224
Separate-Indexing
Pre-Characterization:
Need to measure the phase offset.
Need to measure the gain and phase profiles so we can predict accurately the index needed to go to a certain gain and phase.
Ignore DC offset as DC offset for this type of variable-gain phase shifter is small.
  The effect of DC offset will by captured by the profiles as long as the DC offset doesn’t exceed the smallest gain circle.

## Slide 225
Separate-Indexing: Phase Index-Mapping
Gain index: i Phase index: j
cartesian point from measuring gain and phase index of i and j

## Slide 226
Phase Offset:
Phase reference is set to the phase of the measurement injection signal.
Phase delay from the injection signal to the measurement instrument causes global phase offset.
j = 0
Separate-Indexing: Phase Index-Mapping

## Slide 227
Phase Offset Measurement:
For each gain circle, set the ideal point to be of phase 0.
Measure this point and calculate the phase of the measured point.
Iteratively compensate for this phase offset until the measured phase is smaller than the actual phase resolution.
Separate-Indexing: Phase Index-Mapping

## Slide 228
Phase Offset Compensation:
Subtract the targeting phase by the phase offset.
Separate-Indexing: Phase Index-Mapping

## Slide 229
Separate-Indexing
Gain profile and phase profile:
Need pre-characterization to build an index-to-gain/phase profile to accurately model the relationship between gain/phase and index variation.
For reducing the number of measurement in pre-characterization, the profile needs to be based on general phenomena thus it could be applied in different occasions.
The profile doesn’t have to be precise, but it need to put the measurement point in the vicinity of the kernel search area of the ideal point thus a solution can converge quickly.

## Slide 230
Separate-Indexing: Pre-Characterization
We expect some phase offset and it will be compensated at every targeting gain circle
Sampling Gain index: {round(linspace(1,end,steps))}
Sampling Phase index: {1} (arbitrary)

## Slide 231
Separate-Indexing: Pre-Characterization
Sampling Gain index: {round(linspace(1,end,steps))}
cartesian point from measuring gain and phase index of i and j
Sampling Phase index: {1} (arbitrary)

## Slide 232
Separate-Indexing: Pre-Characterization

## Slide 233
Separate-Indexing: Pre-Characterization

## Slide 234
Separate-Indexing: Pre-Characterization

## Slide 235
Separate-Indexing: Pre-Characterization
Sampling Gain index: {end}
Sampling Phase index: {round(linspace(1,end,steps))}
……

## Slide 236
Separate-Indexing: Pre-Characterization
Sampling Gain index: {end}
Sampling Phase index: {round(linspace(1,end,end))}
……
Note that the phase index “j” is treated as a constant

## Slide 237
Separate-Indexing: Pre-Characterization
***
The gain profile assumes the lowest gain circle follows the footprint of the largest gain circle.
The larger the phase variation with gain, the less linearly-scalable the gain profile is.
More complicated gain profile translation technique is needed if the phase variation is large and you intent to calibrate for gain circles very close to the lowest available gain.

## Slide 238
Separate-Indexing: Pre-Characterization
***
The gain profile assumes the lowest gain circle follows the footprint of the largest gain circle.
The larger the phase variation with gain, the less linearly-scalable the gain profile is.
More complicated gain profile translation technique is needed if the phase variation is large and you intent to calibrate for gain circles very close to the lowest available gain.
This effect can be ignored if the lowest gain circle is very small.

## Slide 239
Separate-Indexing: Pre-Characterization
Constant phase lines
Constant gain circles
What about phase profile?
Phase profile often changes with phase, which makes it unscalable.

## Slide 240
Separate-Indexing: Pre-Characterization
What about phase profile?
Phase profile often changes with phase, which makes it unscalable.
If maximum phase variation in between gain indexes are less than the targeting phase resolution (small enough for kernel search), then phase profile is unnecessary.

## Slide 241
Separate-Indexing: Pre-Characterization
What about phase profile?
Phase profile often changes with phase, which makes it unscalable.
If maximum phase variation in between gain indexes are less than the targeting phase resolution (small enough for kernel search), then phase profile is unnecessary.
Leave phase variation to kernel search or use machine learning.

## Slide 242
Separate-Indexing: Machine Learning
Use machine learning as another way of translating targeting position to index.
Machine learning model, if properly trained, can accurately model non-idealities that would otherwise be difficult to model by pre-characterization.
The machine learning model should be trained on a general dataset of a type of variable-gain phase-shifters that all exhibit similar behaviors so the model could quickly adapt to a specific device.

## Slide 243
Separate-Indexing: Machine Learning
Use machine learning as another way of translating targeting position to index.
Machine learning model, if properly trained, can accurately model non-idealities that would otherwise be difficult to model by pre-characterization.
The machine learning model should be trained on a general dataset of a type of variable-gain phase-shifters that all exhibit similar behaviors so the model could quickly adapt to a specific device.
Use normalized values for training so that the model can be easily applied to different devices.
Normalized Phase-Corrected Measurement Polar Coordinates

## Slide 244
Separate-Indexing: Machine Learning
Why train on phase-corrected dataset?
The model should be applicable no matter the device’s specific phase offset.
For array level implementation, the phase offset need to be known for each gain circle.
Not Phase-corrected
Phase-corrected

## Slide 245
Separate-Indexing: Machine Learning
Phase Offset Compensation:
Subtract the targeting phase by the phase offset.

## Slide 246
Separate-Indexing: Machine Learning
Trained on 65536 data points
  Randomly shuffled
  0.7 train, 0.15 val, 0.15 test
Trained on CPU using MATLAB fitnet and default options
  The optimization function supported on GPU produce worse result
Hidden layer size of 15 is chosen for best observed performance
~ 88% first point accuracy

## Slide 247
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 248
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 249
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 250
Vector-Sum

## Slide 251
Vector-Sum
Ideal case:
Constellation is square and is centered at 0

## Slide 252
Vector-Sum
Ideal case:
Constellation is square and is centered at 0
Two vectors are perpendicular to each other, and the origin is at 0

## Slide 253
Vector-Sum
Ideal case:
Constellation is square and is centered at 0
Two vectors are perpendicular to each other, and the origin is at 0

## Slide 254
Vector-Sum
Ideal case:
Constellation is square and is centered at 0
Two vectors are perpendicular to each other, and the origin is at 0

## Slide 255
Vector-Sum
Realistic case:
Constellation is not square and is not centered at 0
Two vectors are not perpendicular to each other, and the origin is not at 0

## Slide 256
Vector-Sum
[1, 1]
[end, 1]
[1, end]
[end, end]
Realistic case:
Constellation is not square and is not centered at 0
Two vectors are not perpendicular to each other, and the origin is not at 0
The origin of the vectors is often at a corner of the constellation

## Slide 257
Vector-Sum
[1, 1]
[end, 1]
[1, end]
[end, end]
Pre-Characterization:
Need a reference point as the origin of the two vectors.
Need to measure the direction of the two vectors.
  Phase offset information is embedded in the directions of the two vectors.
Need to measure the vector length profiles and the envelop profiles.

## Slide 258
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]

## Slide 259
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The direction of the two vectors should be defined at where the constellation points are the densest.

## Slide 260
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The direction of the two vectors should be defined at where the constellation points are the densest.
Usually this is at the center of the constellation.

## Slide 261
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 262
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
Vector-Sum: Pre-Characterization

## Slide 263
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
Vector-Sum: Pre-Characterization

## Slide 264
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
Vector-Sum: Pre-Characterization

## Slide 265
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
Vector-Sum: Pre-Characterization

## Slide 266
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
Vector-Sum: Pre-Characterization

## Slide 267
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 268
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 269
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 270
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.

## Slide 271
Vector-Sum: Pre-Characterization
A special property of a vector-sum constellation is that the constellation is periodic.
  The constellation looks the same locally wherever in the constellation.
The reference point doesn’t need to be at DC offset
  No need to measure DC offset
  Define reference point at where the points are the densest so that the surrounding vectors are well defined

## Slide 272
Vector-Sum: Pre-Characterization
The direction of the two vectors should be defined at where the constellation points are the densest.
Usually this is at the center of the constellation.
[1, 1]
[end, 1]
[1, end]
[end, end]

## Slide 273
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The direction of the two vectors should be defined at where the constellation points are the densest.
Usually this is at the center of the constellation.
Define reference point at the center index position
[1, middle]
[end, middle]
[middle, 1]
[middle, end]
[middle, middle]
The reference index need to be the common index of the measurements taken to characterize vector1 and vector2 profile.

## Slide 274
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The direction of the two vectors should be defined at where the constellation points are the densest.
Usually this is at the center of the constellation.
Define reference point at the center index position
The reference index need to be the common index of the measurements taken to characterize vector1 and vector2 profile.

## Slide 275
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
With the reference point and the directions of the two vectors known, we can decompose any vectors into these two directions.

## Slide 276
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
With the reference point and the directions of the two vectors known, we can decompose any vectors into these two directions.

## Slide 277
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
With the reference point and the directions of the two vectors known, we can decompose any vectors into these two directions.

## Slide 278
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
With the reference point and the directions of the two vectors known, we can decompose any vectors into these two directions.

## Slide 279
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
With the reference point and the directions of the two vectors known, we can decompose any vectors into these two directions.

## Slide 280
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
With the reference point and the directions of the two vectors known, we can decompose any vectors into these two directions.

## Slide 281
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure along the two center lines to:
  Define the reference point
  Define the two vector directions
  Model the index-to-vector length profiles

## Slide 282
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]

## Slide 283
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]

## Slide 284
Vector-Sum: Pre-Characterization
  Sample the vector in multiple parts for generalization.

## Slide 285
Vector-Sum: Pre-Characterization
  Sample the vector in multiple parts for generalization.

## Slide 286
Vector-Sum: Pre-Characterization
)

## Slide 287
Vector-Sum: Pre-Characterization
)

## Slide 288
Vector-Sum: Pre-Characterization
Transformation from a profile of positions to a profile of vector length referencing the reference point
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((1))−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟2 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((2))−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|

## Slide 289
Vector-Sum: Pre-Characterization
Transformation from a profile of positions to a profile of vector length referencing the reference point
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((1))−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟2 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((2))−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|

## Slide 290
Vector-Sum: Pre-Characterization
Transformation from a profile of positions to a profile of vector length referencing the reference point
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((1))−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟2 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((2))−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|

## Slide 291
Vector-Sum: Pre-Characterization
Transformation from a profile of positions to a profile of vector length referencing the reference point
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((1))−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟2 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((2))−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|

## Slide 292
Vector-Sum: Pre-Characterization
Transformation from a profile of positions to a profile of vector length referencing the reference point
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((1))−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟2 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((2))−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)

## Slide 293
Vector-Sum: Pre-Characterization
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)

## Slide 294
Vector-Sum: Pre-Characterization
Transformation from a profile of positions to a profile of vector length referencing the reference point
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((1))−𝑣𝑒𝑐𝑡𝑜𝑟1 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟2 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)
= |𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
−|𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒((2))−𝑣𝑒𝑐𝑡𝑜𝑟2 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(1)|
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ 𝑝𝑟𝑜𝑓𝑖𝑙𝑒(𝑖)

## Slide 295
Vector-Sum: Pre-Characterization
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ
= 𝑣𝑒𝑐𝑡𝑜𝑟1𝐿𝑒𝑛𝑔𝑡ℎ2𝑖𝑛𝑑𝑒𝑥()
= round(𝑖𝑛𝑡𝑒𝑟𝑝𝑜𝑙𝑎𝑡𝑒(
= 𝑣𝑒𝑐𝑡𝑜𝑟2𝐿𝑒𝑛𝑔𝑡ℎ2𝑖𝑛𝑑𝑒𝑥()
=round(𝑖𝑛𝑡𝑒𝑟𝑝𝑜𝑙𝑎𝑡𝑒()

## Slide 296
Vector-Sum: Pre-Characterization
𝑣𝑒𝑐𝑡𝑜𝑟1 𝑙𝑒𝑛𝑔𝑡ℎ
= 𝑣𝑒𝑐𝑡𝑜𝑟1𝐿𝑒𝑛𝑔𝑡ℎ2𝑖𝑛𝑑𝑒𝑥()
= round(𝑖𝑛𝑡𝑒𝑟𝑝𝑜𝑙𝑎𝑡𝑒(
= 𝑣𝑒𝑐𝑡𝑜𝑟2𝐿𝑒𝑛𝑔𝑡ℎ2𝑖𝑛𝑑𝑒𝑥()
=round(𝑖𝑛𝑡𝑒𝑟𝑝𝑜𝑙𝑎𝑡𝑒()

## Slide 297
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The vector envelope changes as the other vector length changes.

## Slide 298
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The vector envelope changes as the other vector length changes.

## Slide 299
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The vector envelope changes as the other vector length changes.

## Slide 300
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The vector envelope changes as the other vector length changes.
Need to scale the vector length profile according to the vector length of the other vector.

## Slide 301
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The vector envelope changes as the other vector length changes.
Need to scale the vector length profile according to the vector length of the other vector.
But the vector length of the other vector also depend on the vector length of this vector.

## Slide 302
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
The vector envelope changes as the other vector length changes.
Need to scale the vector length profile according to the vector length of the other vector.
But the vector length of the other vector also depend on the vector length of this vector.
Due to the inter-dependency of the vector length, we cannot measure the vector envelope profile directly as a function of an individual vector length.

## Slide 303
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 304
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 305
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 306
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 307
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Measure the envelope points and decompose them into the two vector directions.
Make mapping between the two decomposed vector lengths.

## Slide 308
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Individually scale each side of the constellation for maximum accuracy.

## Slide 309
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Individually scale each side of the constellation for maximum accuracy.

## Slide 310
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Individually scale each side of the constellation for maximum accuracy.

## Slide 311
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Individually scale each side of the constellation for maximum accuracy.

## Slide 312
Vector-Sum: Pre-Characterization
[1, 1]
[end, 1]
[1, end]
[end, end]
Individually scale each side of the constellation for maximum accuracy.

## Slide 313
Vector-Sum: Pre-Characterization

## Slide 314
Vector-Sum: Pre-Characterization
)
)
L2 is treated as a constant

## Slide 315
Vector-Sum: Pre-Characterization
)
)
)
)

## Slide 316
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 317
Point Translation
Outphasing
Separate-Indexing
Vector-Sum

## Slide 318
Point Translation

## Slide 319
Point Finding

## Slide 320
Point Finding
Coming Soon

## Slide 321: Point Finding
  Kernel Size
Search Area
A N-by-N grid of ideal points used to find the closest measurement point to the targeting position.
N is called kernel size
  N=1, 3, 5, 7, ……

## Slide 322: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Development Update 5

## Slide 323
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Measurement
Measurement Point Position
Point Finding
Next*

## Slide 324
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Unique for different types of variable gain phase shifters
Provides a first guess of the code/index
Established through:
  Pre-characterization
    DC offset, vector length, phase offset, index-to-position profile
  Machine Learning

## Slide 325
Calibration Mechanism
Next ideal Point Position
Point Finding
Measurement
Same for different types of variable gain phase shifters (it’s based on cartesian coordinates)
Only needed if the first guess doesn’t satisfy specified requirements
Include:
  Measurement filtering and validation
  Adaptive kernel search
  Kernel space mapping

## Slide 326
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Measurement
Measurement Point Position
Point Finding
Next*

## Slide 327
Unvalidated Calibration
Ideal Point Position
Point Translation
Code/Index
Once Point Translation is established through pre-characterization algorithm or machine learning, the point translation algorithm computes LUT for all the ideal points.
Much fewer measurements needed for calibration.
Worse result than validated calibration.
Need accurate translation since we are not relying on kernel search.