## Slide 1: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen

## Slide 2: Traditional Method
IC
PC
Computer sends all settings to the DUT (in arbitrary order) for measurement.
A constellation of all settings is generated.
Computer scans all constellation points to find the point closest to the ideal position and establish the mapping.
Advantage:
Highest accuracy and often guaranteed solution.
Measurement order and details of the controls are hidden from the user.
Relaxed requirement for the DUT gain and phase response.
Disadvantage:
Long measurement time and long post-processing time. (Need to measure every point and computer need to scan every point for comparison for every ideal points)

## Slide 3: Adaptive Measurements

## Slide 4: Adaptive Measurements

## Slide 5: Adaptive Measurements
Need bi-directional relationship from DUT settings to the measurement points.
DUT response need to be predictable, and the measurement results need to be near the ideal points.

## Slide 6: Outphasing Phase Shifter

## Slide 7: Outphasing Phase Shifter

## Slide 8: Outphasing Phase Shifter

## Slide 9: Outphasing Phase Shifter

## Slide 10: Outphasing Phase Shifter

## Slide 11: Outphasing Phase Shifter

## Slide 12: Outphasing Phase Shifter

## Slide 13: Outphasing Phase Shifter

## Slide 14: Outphasing Phase Shifter

## Slide 15: Outphasing Phase Shifter
Vector Phases to Cartesian:
Cartesian to Vector Phases:
(using inverse kinematic)

## Slide 16: Outphasing Phase Shifter
Vector Phases to Cartesian:
Cartesian to Vector Phases:
(using inverse kinematic)

## Slide 17: RFVM
Vector lengths to Cartesian:
Cartesian to Vector lengths:

## Slide 18: Adaptive Measurements
ideal target point
For an ideal target point, use inverse kinematic to calculate the corresponding two vector phases and obtain the measurements.

## Slide 19: Adaptive Measurements
ideal target point
For an ideal target point, use inverse kinematic to calculate the corresponding two vector phases and obtain the measurements.
measurements
If measure all the points for a constant gain circle at once, the distorted circle makes adjustment difficult and reductant measurements are made.

## Slide 20: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0

## Slide 21: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 22: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 23: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 24: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 25: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 26: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.

## Slide 27: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.

## Slide 28: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.

## Slide 29: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution)

## Slide 30: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution)

## Slide 31: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.

## Slide 32: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.

## Slide 33: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
  is targeting point inside the measurement results boundary?

## Slide 34: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 35: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 36: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 37: Point-to-Point Progressive Measurements

## Slide 38: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 39: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 40: RTPS Phase Switching Modes
RTPS 1
RTPS 2
RTPS 3
RTPS 1
RTPS 2
RTPS 3

## Slide 41: RTPS Phase Switching Modes

## Slide 42: RTPS Phase Switching Modes

## Slide 43: RTPS Phase Switching Modes

## Slide 44: RTPS Phase Switching Modes
RTPS 1
RTPS 2
RTPS 3
RTPS 1
RTPS 2
RTPS 3
9 Modes for a pair of phase setting.
Due to PVT variation and mismatch, the constellation of the 9 modes are slightly different.
Provide fine tune to the constellation point.
Due to the random nature of this variation, this effect cannot be learned.

## Slide 45: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 46: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 47: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.

## Slide 48: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.

## Slide 49: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.

## Slide 50: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.
  Establish mapping between the codeword of the closest point to the position of the ideal point.

## Slide 51: Point-to-Point Progressive Measurements
Phase offset compensation
  Target an ideal point of phase 0
  Iteratively adjust phase offset so that the measurement point aligns with the target point.
Next point calibration
  Increment the ideal point by the target phase resolution.
  Perform measurements in the search area (± actual phase resolution and ± actual gain resolution).
  Find the measurement point in the search area that is closet to the ideal point.
  In the case of deviating measurements, a test is performed to evaluate the search area measurement validity.
    The error vectors for every ideal/measurement pair are averaged and a new search area is found in the opposite direction.
  Measure the 9 modes and find the closest point to the ideal point.
  Establish mapping between the codeword of the closest point to the position of the ideal point.
  Repeat 2 until all ideal points on this gain circle are calibrated.

## Slide 52: Point-to-Point Progressive Measurements
Remarks:
Progressive measurement is repeated for every needed constant gain circle.
The step of phase offset compensation should be done after DC offset compensation and vector length measurement.
All measurement results in the search area are saved so that there is no need for repetitive measurement when accessed again.

## Slide 53: Accelerated Measurement Prediction

## Slide 54: Accelerated Measurement Prediction

## Slide 55: Accelerated Measurement Prediction

## Slide 56: Accelerated Measurement Prediction

## Slide 57: Accelerated Measurement Prediction
Mapping

## Slide 58: Accelerated Measurement Prediction

## Slide 59: Accelerated Measurement Prediction

## Slide 60: Accelerated Measurement Prediction

## Slide 61: Accelerated Measurement Prediction

## Slide 62: Accelerated Measurement Prediction

## Slide 63: Accelerated Measurement Prediction

## Slide 64: Accelerated Measurement Prediction

## Slide 65: Accelerated Measurement Prediction

## Slide 66: Accelerated Measurement Prediction
Target Position
Ideal Position that results in the closest measurement to the target position

## Slide 67: Accelerated Measurement Prediction
Target Position
Ideal Position that results in the closest measurement to the target position
In-situ training and validating

## Slide 68: Accelerated Measurement Prediction

## Slide 69: Accelerated Measurement Prediction

## Slide 70: Accelerated Measurement Prediction

## Slide 71: Accelerated Measurement Prediction

## Slide 72: Accelerated Measurement Prediction
Target Position
Ideal Position that results in the closest measurement to the target position
In-situ training and validating
Progressive training per gain circle.
Neural Network replaces the normal routine after making 5 correct prediction in a row.
When the network is not validated, a new targeting point is fed to the neural network for testing before it is used for training so that the testing data has not been trained by the network.
Neural Network prediction is verified by doing the 9 mode measurements and judge if the closet point is close enough (by previous standard).
If Neural Network prediction is checked to be inaccurate, the current targeting point is calibrated using the normal routine and the neural network restart training.

## Slide 74: Thank you

## Slide 75: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Development Update 1

## Slide 76
Measurement non-uniformity causes distortion in constant gain circle

## Slide 77
Measurement Dead zones

## Slide 78: Demo