## Slide 1: An Adaptive Calibration Algorithm Using Progressive Measurement and Accelerated Measurement Prediction
Yuxuan Chen
Development Update 5

## Slide 2
# measurements: 6947
Phase RMSE: 0.92304°
Gain RMSE: -20.5574 dB
Outphasing
# measurements: 1233
Phase RMSE: 0.75647°
Gain RMSE: -32.6778 dB
Separate-Indexing
Supervised Calibration
Vector-Sum
# measurements: 618
Phase RMSE: 1.2445°
Gain RMSE: -24.1766 dB

## Slide 3
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Measurement
Measurement Point Position
Point Finding
Next*

## Slide 4
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Unique for different types of variable gain phase shifters
Provides a first guess of the code/index
Established through:
  Pre-characterization
    DC offset, vector length, phase offset, index-to-position profile
  Machine Learning

## Slide 5
Calibration Mechanism
Next ideal Point Position
Point Finding
Measurement
Same for different types of variable gain phase shifters (it’s based on cartesian coordinates)
Only needed if the first guess doesn’t satisfy specified requirements
Include:
  Measurement filtering and validation
  Adaptive kernel search
  Kernel space mapping

## Slide 6
Calibration Mechanism
Ideal Point Position
Point Translation
Code/Index
Measurement
Measurement Point Position
Point Finding
Next*

## Slide 7
Unsupervised Calibration
Ideal Point Position
Point Translation
Code/Index
Once Point Translation is established through pre-characterization algorithm or machine learning, the point translation algorithm computes LUT for all the ideal points.
Much fewer measurements needed for calibration.
Worse result than validated calibration.
Need accurate translation since we are not relying on kernel search.

## Slide 8
# measurements: 1134
Phase RMSE: 0.59674°
Gain RMSE: -32.3763 dB
Separate-Indexing with gain and phase profile
Improved Separate-Indexing Pre-Characterization
# measurements: 1233
Phase RMSE: 0.75647°
Gain RMSE: -32.6778 dB
Separate-Indexing
with gain profile

## Slide 9
# measurements: 168
Phase RMSE: 3.1282°
Gain RMSE: -14.5345 dB
Hit rate: 7.0312%
Outphasing
# measurements: 265
Phase RMSE: 1.9125°
Gain RMSE: -25.5734 dB
Hit rate: 33.3984%
Separate-Indexing
Unsupervised Calibration
Vector-Sum
# measurements: 111
Phase RMSE: 1.2445°
Gain RMSE: -24.1766 dB
Hit rate: 100%

## Slide 10
# measurements: 6947
Phase RMSE: 0.92304°
Gain RMSE: -20.5574 dB
Outphasing
# measurements: 1233
Phase RMSE: 0.75647°
Gain RMSE: -32.6778 dB
Separate-Indexing
Supervised Calibration
Vector-Sum
# measurements: 618
Phase RMSE: 1.2445°
Gain RMSE: -24.1766 dB

## Slide 11
Unsupervised Calibration using Machine Learning
Instead of fitting data to pre-defined functions, we can use machine learning to learn any arbitrary constellation behaviours.
Using randomly sampled measurements, a model can be trained and be used as the pre-characterization algorithm.
Since the dataset is limited, we need to transform training data into periodic space to improve the result.
Input and output of the model are the normalized real and imaginary parts of the points.

## Slide 12
# measurements: 753
Phase RMSE: 1.0627°
Gain RMSE: -27.2701 dB
Separate-Indexing
Vector-Sum
# measurements: 540
Phase RMSE: 1.0733°
Gain RMSE: -46.0226 dB
Unsupervised Calibration using Machine Learning

## Slide 13
Unsupervised Calibration using Machine Learning
Separate-Indexing
gain rmse vs sample size
Separate-Indexing
phase rmse vs sample size

## Slide 14
Unsupervised Calibration using Machine Learning
Vector-Sum
gain rmse vs sample size
Vector-Sum
phase rmse vs sample size